## Slide 1: DCTCP vs. Swift: Congestion Control in Data Centers
Computer Networks 236340 – Winter 2024/25
Yasmin Mitkal , Omar Garah, Amir Watted
Advisor: Eran Tavor
Data centers require low latency & high throughput.
Traditional TCP struggles in shallow-buffer environments.
Goal: Improve performance with smarter congestion control.
Different approaches: ECN & delay-based protocols.

## Slide 2: Motivation
Data centers require low latency & high throughput.
Traditional TCP struggles in shallow-buffer environments.
Goal: Improve performance with smarter congestion control.
Different approaches: ECN & delay-based protocols.
  No RFC standard for Swift.
DCTCP vs. Swift: Congestion Control in Data Centers
Computer Networks 236340 – Winter 2024/25
Yasmin Mitkal , Omar Garah, Amir Watted
Advisor: Eran Tavor

## Slide 3: Project Goals
Design and implement a comprehensive comparative performance analysis between SWIFT and DCTCP.
Motivation
Data centers require low latency & high throughput.
Traditional TCP struggles in shallow-buffer environments.
Goal: Improve performance with smarter congestion control.
Different approaches: ECN & delay-based protocols.
Steps Toward the Goal/Project Breakdown
Understand the core principles of DCTCP and Swift.
Ramp up and configure the NS-3 simulator.
Build a fat-tree topology in NS-3.
Analyze the existing implementation of DCTCP in NS-3.
Implement the Swift protocol within NS-3.
Design and run simulations under varying load levels and traffic patterns.
Compare DCTCP and Swift performance
across different scenarios.
Chart: Average Throughput as a function of Number of Flows
| 100 | 250 | 500 | 750 | 1000 | 1500 | 2000
dctcp | 5296.13 | 2204.8733 | 1341.48 | 1006.1743 | 790.7285 | 579.932 | 446.417
Swift (baseRTT + ε) | 5303.25 | 2414.7167 | 1440.53 | 1096.1467 | 885.8943 | 582.3243 | 442.6827
Swift (baseRTT) | 5308.03 | 2414.2267 | 1442 | 1104.21 | 887.8583 | 593.538 | 453.2437
Swift (target_delay = 0.025) | 4981.11 | 2191.4467 | 1303.31 | 958.744 | 752.774 | 554.5587 | 417.8403

## Slide 4: Steps Toward the Goal/Project Breakdown
Understand the core principles of DCTCP and Swift.
Ramp up and configure the NS-3 simulator.
Build a fat-tree topology in NS-3.
Analyze the existing implementation of DCTCP in NS-3.
Implement the Swift protocol within NS-3.
Design and run simulations under varying load levels and traffic patterns.
Compare DCTCP and Swift performance across different scenarios.
Project Goals
Design and implement a comprehensive comparative performance analysis between SWIFT and DCTCP.
Chart: Average Throughput as a function of Number of Flows
| 100 | 250 | 500 | 750 | 1000 | 1500 | 2000
dctcp | 5296.13 | 2204.8733 | 1341.48 | 1006.1743 | 790.7285 | 579.932 | 446.417
Swift (baseRTT + ε) | 5303.25 | 2414.7167 | 1440.53 | 1096.1467 | 885.8943 | 582.3243 | 442.6827
Swift (baseRTT) | 5308.03 | 2414.2267 | 1442 | 1104.21 | 887.8583 | 593.538 | 453.2437
Swift (target_delay = 0.025) | 4981.11 | 2191.4467 | 1303.31 | 958.744 | 752.774 | 554.5587 | 417.8403
ECN marking at threshold K.
Multi-bit feedback from ECN by tracking fraction of marked packets (α)->represents the extent of congestion.
Window adjustment proportional to extent of congestion.
Retains TCP behaviors
(slow start, additive increase, loss recovery).
Sender 1
Sender 2
ECN Mark (1bit)
Receiver

## Slide 5: Theoretical Background

## Slide 6: DCTCP Overview
ECN marking at threshold K.
Multi-bit feedback from ECN by tracking fraction of marked packets (α)->represents the extent of congestion.
Window adjustment proportional to extent of congestion.
Retains TCP behaviors
(slow start, additive increase, loss recovery).
Sender 1
Sender 2
ECN Mark (1bit)
Receiver
DCTCP Algorithm
Switches mark incoming packets with CE when queue occupancy exceeds parameter K.
The Receiver Sets the ECN-Echo flag in ACKs to notify the sender of congestion until the sender acknowledges with a CWR flag.
The receiver aims to reflect the exact pattern of marked packets, enabling accurate estimation of congestion at the sender.
The sender computes α (fraction of marked packets) and adjusts the cwnd proportionally:
  Larger α → more aggressive window reduction
  Smaller α → gentler adjustment
α (1-g) x α + g x F
cwnd cwnd x (1- α / 2)

## Slide 7: DCTCP Algorithm
Switches mark incoming packets with CE when queue occupancy exceeds parameter K.
The Receiver Sets the ECN-Echo flag in ACKs to notify the sender of congestion until the sender acknowledges with a CWR flag.
The sender computes α (fraction of marked packets) and adjusts the cwnd proportionally:
  Larger α → more aggressive window reduction
  Smaller α → gentler adjustment
Sender 1
Sender 2
ECN Mark (1bit)
Receiver
DCTCP Overview
ECN marking at threshold K.
Multi-bit feedback from ECN by tracking fraction of marked packets (α)->represents the extent of congestion.
Window adjustment proportional to extent of congestion.
Retains TCP behaviors
(slow start, additive increase, loss recovery).
Swift Overview

## Slide 8: DCTCP Algorithm
Delay-based congestion control.
Employs a simple AIMD controller to maintain a target delay.
Uses delay (RTT) as the primary congestion signal instead of loss or ECN.
Delay is decomposed into fabric and endpoint.
Scales target delay dynamically based on:
  Topology
  Flow load
Swift Overview
Switches mark incoming packets with CE when queue occupancy exceeds parameter K.
The Receiver Sets the ECN-Echo flag in ACKs to notify the sender of congestion until the sender acknowledges with a CWR flag.
The receiver aims to reflect the exact pattern of marked packets, enabling accurate estimation of congestion at the sender.
The sender computes α (fraction of marked packets) and adjusts the cwnd proportionally:
  Larger α → more aggressive window reduction
  Smaller α → gentler adjustment
α (1-g) x α + g x F
cwnd cwnd x (1- α / 2)
Swift Algorithm

## Slide 9
Swift Algorithm
Delay-based congestion control.
Employs a simple AIMD controller to maintain a target delay.
Uses delay (RTT) as the primary congestion signal instead of loss or ECN.
Delay is decomposed into fabric and endpoint.
Scales target delay dynamically based on:
  Topology
  Flow load
Swift Overview
DCTCP in NS-3
DCTCP is implemented as an extension of standard TCP in NS-3.
Follows original paper’s logic, with key additions such as:
PktsAcked() override: updates α using ECN-marked ACKs.
Used RED queues with ECN.
Fine tuned K.
Insight: Tuning K impacts fairness.

## Slide 10: BBR vs Swift
BBR tries to set cwnd to the product of the estimated maximum bandwidth and the minimum RTT (the pure propagation delay).
Swift, on the other hand, defines a target delay and then continuously adjusts the cwnd so that the actual RTT stays close to this target.

## Slide 11
DCTCP in NS-3
DCTCP is implemented as an extension of standard TCP in NS-3.
Follows original paper’s logic, with key additions such as:
PktsAcked() override: updates α using ECN-marked ACKs.
Used RED queues with ECN.
Fine tuned K.
Insight: Tuning K impacts fairness.
Swift Algorithm

## Slide 12
Challenges in Implementing Swift
Not everything about Swift is clearly defined for example, how to handle the slow start phase was unclear.
We had to fully understand and dive into the entire TCP stack in NS-3 in order to integrate Swift correctly.
Swift Algorithm

## Slide 13
Swift in NS-3 (Implementation)
Implemented Swift as a subclass of TcpNewReno.
Added fields: alpha, beta, min_cwnd, max_cwnd.
Implemented a function that estimates Target delay.
Overrode key functions:
  IncreaseWindow: compares measured delay vs. target delay
  Retransmit
  EnterRecovery
Used existing TcpSocketState fields:
  RTT
  PacingRate
DCTCP in NS-3
DCTCP is implemented as an extension of standard TCP in NS-3.
Follows original paper’s logic, with key additions such as:
PktsAcked() override: updates α using ECN-marked ACKs.
Used RED queues with ECN.
Fine tuned K.
Insight: Tuning K impacts fairness.
Configuration Challenges & Fairness Considerations
Fair Comparison with DCTCP
Parameter Tuning
Target Delay Configuration

## Slide 14
Configuration Challenges & Fairness Considerations
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Fair Comparison with DCTCP
Parameter Tuning
Target Delay Configuration
Swift in NS-3 (Implementation)
Implemented Swift as a subclass of TcpNewReno.
Added fields: alpha, beta, min_cwnd, max_cwnd.
Overrode key functions:
  IncreaseWindow: compares measured delay vs. target delay
  Retransmit
  EnterRecovery
Used existing TcpSocketState fields:
  RTT
  PacingRate

## Slide 15
Configuration Challenges & Fairness Considerations
Fair Comparison with DCTCP
Parameter Tuning
Target Delay Configuration
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.

## Slide 16
Configuration Challenges & Fairness Considerations
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Fair Comparison with DCTCP
Parameter Tuning
Target Delay Configuration
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values

## Slide 17
Configuration Challenges & Fairness Considerations
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Fair Comparison with DCTCP
Parameter Tuning
Target Delay Configuration
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)

## Slide 18
Average Throughput (kbps)
Average Delay (s)
Average Packet Loss Rate(%)
Configuration Challenges & Fairness Considerations
Fair Comparison with DCTCP
Parameter Tuning
Target Delay Configuration
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Target Delay Impact

## Slide 19
Best Strategy:
Insights:
Using minimum observed RTT as the target delay.
Achieved best balance
Confirms trade-off from Swift paper: larger delay boosts throughput; smaller delay reduces latency.
Our results show throughput peaks then drops as target delay increases (unlike paper).
min_cwnd Impact:
Too small → slow recovery after congestion.
Too large → high queuing, increased delay, and packet loss
Needs careful tuning to avoid over- or under-reacting.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)

## Slide 20
min_cwnd Impact:
Too small → slow recovery after congestion.
Too large → high queuing, increased delay, and packet loss
Needs careful tuning to avoid over- or under-reacting.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)
Best Strategy:
Insights:
Using minimum observed RTT as the target delay.
Achieved best balance
Confirms trade-off from Swift paper: larger delay boosts throughput; smaller delay reduces latency.
Our results show throughput peaks then drops as target delay increases (unlike paper).
Simulation Setup
Fat-tree topology in NS-3.
Multiple traffic modes.
Metrics: Throughput, Delay, Packet Loss.
Averaged over 3 runs per data point.

## Slide 21
min_cwnd Impact:
Too small → slow recovery after congestion.
Too large → high queuing, increased delay, and packet loss
Needs careful tuning to avoid over- or under-reacting.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)
Best Strategy:
Insights:
Using minimum observed RTT as the target delay.
Achieved best balance
Confirms trade-off from Swift paper: larger delay boosts throughput; smaller delay reduces latency.
Our results show throughput peaks then drops as target delay increases (unlike paper).
Simulation Setup
Fat-tree topology in NS-3.
Multiple traffic modes.
Metrics: Throughput, Delay, Packet Loss.
Averaged over 3 runs per data point.

## Slide 22
min_cwnd Impact:
Too small → slow recovery after congestion.
Too large → high queuing, increased delay, and packet loss
Needs careful tuning to avoid over- or under-reacting.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)
Best Strategy:
Insights:
Using minimum observed RTT as the target delay.
Achieved best balance
Confirms trade-off from Swift paper: larger delay boosts throughput; smaller delay reduces latency.
Our results show throughput peaks then drops as target delay increases (unlike paper).
Simulation Setup
Fat-tree topology in NS-3.
Multiple traffic modes.
Metrics: Throughput, Delay, Packet Loss.
Averaged over 3 runs per data point.
Hypothesis: dropping packets locally before they ever reach the wire.

## Slide 23: Simulation Setup
Fat-tree topology in NS-3.
Multiple traffic modes.
Metrics: Throughput, Delay, Packet Loss.
On-off application
Averaged over 3 runs per data point.
3 swift variants:-
  Static target delay – 25ms
  Target delay is base rtt (min rtt observed)
  Base rtt + ~ 1ms
Fat-tree topology in NS-3.
Multiple traffic modes.
Metrics: Throughput, Delay, Packet Loss.
Averaged over 3 runs per data point.
min_cwnd Impact:
Too small → slow recovery after congestion.
Too large → high queuing, increased delay, and packet loss
Needs careful tuning to avoid over- or under-reacting.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)

## Slide 24: Disclaimer: swift paper setup
Swift paper compares against GCN a highly tuned version of DCTCP used by Google.
Traffic control setup in Google’s datacenters is unclear, while we used multiple traffic patterns: hotspot and random pairing.
Goal: Confirm qualitative trends, not exact performance.
Fat-tree topology in NS-3.
Multiple traffic modes.
Metrics: Throughput, Delay, Packet Loss.
Averaged over 3 runs per data point.
min_cwnd Impact:
Too small → slow recovery after congestion.
Too large → high queuing, increased delay, and packet loss
Needs careful tuning to avoid over- or under-reacting.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)

## Slide 25: K=4 (16 hosts) and a 15 seconds simulation runtime mode 1 (random hot spot):

## Slide 26: Zooming in on Throughput

## Slide 27: K=4 (16 hosts) and a 15 seconds simulation runtime mode 2 (random pairing):

## Slide 28: Zooming in on Throughput

## Slide 29: K=12 (432 hosts) and a 7 seconds simulation runtime mode 1 (random hot spot):

## Slide 30: Zooming in on Throughput

## Slide 31
Discussion of Results
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Delay
Packet Loss
Throughput
Swift in NS-3 (Implementation)
Implemented Swift as a subclass of TcpNewReno.
Added fields: alpha, beta, min_cwnd, max_cwnd.
Overrode key functions:
  IncreaseWindow: compares measured delay vs. target delay
  Retransmit
  EnterRecovery
Used existing TcpSocketState fields:
  RTT
  PacingRate

## Slide 32
Discussion of Results
Delay
Packet Loss
  Swift (0.025 delay) had best throughput in low congestion. Under high congestion, it performed worst.
  Small topologies: Swift (baseRTT) outperformed.
  Large topologies: DCTCP slightly better.
  Swift (baseRTT) and DCTCP are nearly equivalent in throughput under high congestion.
Throughput

## Slide 33
Discussion of Results
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Delay
Packet Loss
Throughput
  Swift (0.025 delay) had highest loss.
  Swift (baseRTT) had lowest loss.
  Swift (baseRTT + ɛ) slightly worse than baseRTT but better than fixed delay.
  baseRTT keeps window small, minimize queuing and packet loss.

## Slide 34
Discussion of Results
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Delay
Packet Loss
Throughput
  Swift (baseRTT): Lowest delay in low/moderate congestion (mode 2).
  In high congestion DCTCP showed lower delay than baseRTT.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)

## Slide 35: Comparison with Swift’s Paper Results
We claim:
Dctcp generally has Lower delay
Comparable throughput
Lower loss
Static delays perform poorly.
Swift paper claims:
Lower delay than GCN
Comparable throughput
Lower loss, especially at the tail
Static delays perform poorly.

## Slide 36
Our Results vs. Swift’s Paper
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Delay
Packet Loss
Throughput
Swift in NS-3 (Implementation)
Implemented Swift as a subclass of TcpNewReno.
Added fields: alpha, beta, min_cwnd, max_cwnd.
Overrode key functions:
  IncreaseWindow: compares measured delay vs. target delay
  Retransmit
  EnterRecovery
Used existing TcpSocketState fields:
  RTT
  PacingRate

## Slide 37
Our Results vs. Swift’s Paper
Delay
Packet Loss
Throughput
  Matches Swift paper trends:
  Swift (baseRTT) ~ DCTCP in throughput.
  Swift (0.025 delay) best in low congestion.
  DCTCP slightly better in high congestion (k=12)

## Slide 38
Our Results vs. Swift’s Paper
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Delay
Packet Loss
Throughput
  Strong alignment with Swift paper:
  Swift (baseRTT) had lowest loss.
  Swift (0.025 delay) performed worst under load confirms static target delay warning

## Slide 39
Our Results vs. Swift’s Paper
  Used static target delay or basertt.
  Dynamic scaling left for future work due to paper ambiguity.
  Many parameters had to be manually tuned.
  Performance highly sensitive to their values.
  Identical RED queues (no ECN for Swift).
  Delay computation limited to fabric delay.
  Matched buffer sizes and traffic load.
Delay
Packet Loss
Throughput
  Partial alignment:
  Swift (baseRTT) had lowest delay in light/moderate congestion.
  DCTCP sometimes had lower delay under high congestion.
  Swift paper consistently shows lower delay for Swift than GCN.
Average Throughput (kbps)
Average Delay
Average Packet Loss Rate(%)

## Slide 40
Throughput & Loss
Swift (baseRTT) and DCTCP showed similar throughput. Swift had lower packet loss, DCTCP maintained lower delay.
Conclusions
Alignment with Swift Paper
Results match Swift’s paper original claims on throughput and loss. However, delay improvements were not fully replicated in our setup.
Importance of Parameter Tuning
Performance is highly sensitive to min_cwnd & target delay. Poor tuning leads to loss and instability.
Target Delay Trade-off
Smaller delays reduce queuing and loss, larger ones boost throughput early but degrade performance under load. baseRTT provides a good balance.
Overall Insight
Swift’s delay-based approach is promising, requires refined tuning of delay targets and pacing.

## Slide 41: Achievements
Implemented Swift in NS-3 and uploaded it to GitHub to support the community.
Fine-tuned Swift parameters for improved performance and stability.
Developed automation tools to streamline simulation and result analysis.
Built a solid base for future projects involving Swift and congestion control protocols.
Compared a new, developing protocol (Swift) against an industry-established protocol (DCTCP).

## Slide 42: Future work
Dynamic Target Delay : Explore adaptive switching between static (0.025s) and baseRTT based on congestion levels.
Hybrid Delay + ECN Signals : Combine ECN with delay-based signaling in Swift .
Fairness Analysis: Conduct detailed fairness comparisons between Swift and DCTCP.
Parameter Auto-Tuning : Automate Swift's parameter tuning using adaptive or learning-based techniques.
Larger-Scale Fat-Tree Topologies : higher k values.
Window Behavior Insights : Analyze congestion window dynamics .
Adaptive baseRTT Recalibration : Periodically update baseRTT to reflect evolving congestion.